## Slide 1
Universität
Münster
ifgi
Institut für Geoinformatik
U-Net Segmentation of Landslides from Drone LiDAR
Nimesh Akalanka · Vijay Kolanchinathan · Md Rafsan Jani
Institut für Geoinformatik (ifgi), University of Münster · Analysis of High Resolution Remote Sensing Imagery, SoSe 2026
Motivation
Landslides cause severe casualties and infrastructure damage across Sri Lanka's central highlands. Post-event mapping is critical for emergency response and risk reduction, yet conventional visual interpretation of drone data is time-consuming and operator-dependent, especially when multiple simultaneous events occur after a single rainfall episode. Deep learning segmentation offers a path toward semi-automated mapping. Its performance depends critically on which input channels are available. This study asks: "Does fusing LiDAR-derived terrain features with RGB imagery improve U-Net landslide segmentation compared to spectral data alone?"
Figure 1: Drone orthomosaic of a Sri Lanka landslide site (site 01, Alawathugoda) showing exposed soil deposit, road disruption, and surrounding vegetation.
Study Area & Dataset
12 post-landslide drone survey sites across Sri Lanka's central highlands: Alawathugoda · Aranayaka (×2) · Hunnasgiriya · Kohowala · Kotmale Kovil Ela · Kundasale · Makehelwala · Kansalagamuwa · Uthuwan Kanda · Victoria Reservoir Input data per site: LiDAR point cloud ground-classified to DTM at 0.1 m grid; RGB orthomosaic at <5 cm GSD; derived layers: Hillshade (azimuth 315°, elevation 45°) and Slope (first-order gradient). Coordinate reference system: EPSG:5235 (Sri Lanka Datum 1999) Train / test split: Sites 01 to 10 = training Sites 11 and 12 = held-out test Tiling and class balance: 256 × 256 px tiles with stride-based sampling. Sites 1,3,5,6,8,9 fully tiled; sites 2,4,7,10 partially tiled. Landslide pixels account for approximately 2% of each scene — severe class imbalance. Labelling: Binary masks (landslide / background) manually delineated per site from orthomosaic and DSM visual inspection.
Methods
Data Processing and Segmentation Pipeline
LiDAR
Point Cloud
DTM
0.1 m grid
Channel Stack
3 – 4 ch
U-Net
256×256
Landslide
Mask
RGB Orthomosaic
Input Configurations
RGB 3 channels: red, green, blue from orthomosaic
RGB + DTM 4 channels: + digital terrain model at 0.1 m
RGB + Hillshade 4 channels: + terrain illumination (independent variant)
RGB + Slope 4 channels: + slope gradient (independent variant)
U-Net Architecture and Training
Architecture: Encoder–decoder (U-Net) with 4 downsampling stages and skip connections that preserve spatial detail. Encoder: 3×3 conv → BatchNorm → ReLU → 2×2 max-pool; feature channels: 64 → 128 → 256 → 512. Bottleneck: 1024-channel deepest representation before decoding. Decoder: Bilinear upsampling ×2 at each stage, concatenated with encoder skip features. Output: 1×1 conv → sigmoid → binary landslide probability map at full input resolution. Training hyperparameters: Optimiser: Adam | Learning rate: 1 × 10⁻⁴ | Batch size: 8 | Epochs: 25 Loss: binary cross-entropy with pos_weight (set to 0.2 — see Discussion) Tile size: 256 × 256 px, stride-based sampling | Prediction stride: 768 px Sigmoid threshold: 0.5 (default, not optimised) Terrain feature derivation: DTM: ground-classified LiDAR rasterised to 0.1 m grid. Hillshade: sun azimuth 315°, elevation 45° (single illumination angle). Slope: first-order gradient magnitude from DTM (degrees). Evaluation: Pixel-level Precision, Recall, and F1-Score on full held-out scenes.
Accuracy is reported but excluded from model selection due to class imbalance.
Training and Validation Loss (early stopping, 21–28 epochs)
Chart: RGB
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
Train | 0.71311 | 0.6298 | 0.61071 | 0.60188 | 0.59072 | 0.57472 | 0.56174 | 0.55224 | 0.52994 | 0.52504 | 0.52067 | 0.51192 | 0.451 | 0.33101 | 0.24823 | 0.21924 | 0.19432 | 0.18544 | 0.17839 | 0.15857 | 0.16328 | 0.14981 | 0.13884 | 0.13629 | 0.13038
Val | 0.64479 | 0.64401 | 0.64946 | 0.63775 | 0.64765 | 0.66762 | 0.6328 | 0.6529 | 0.62873 | 0.68564 | 0.66577 | 0.64162 | 0.52887 | 0.80387 | 0.72231 | 0.5374 | 0.67229 | 0.84024 | 0.53649 | 0.70191 | 0.69374 | 0.85498 | 0.71219 | 0.60433 | 0.72377
Chart: RGB + DTM
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
Train | 0.75905 | 0.67169 | 0.64054 | 0.62588 | 0.60543 | 0.58525 | 0.57197 | 0.5596 | 0.55118 | 0.54576 | 0.53335 | 0.53044 | 0.5241 | 0.5041 | 0.39332 | 0.2744 | 0.22167 | 0.21186 | 0.19837 | 0.18769 | 0.15553 | 0.1512 | 0.13552 | 0.13312 | 0.12496 | 0.13238
Val | 0.7242 | 0.68504 | 0.69595 | 0.68276 | 0.65998 | 0.73402 | 0.63648 | 0.66862 | 0.61904 | 0.67562 | 0.66365 | 0.64977 | 0.6405 | 0.61425 | 0.77832 | 0.65403 | 0.47887 | 0.91731 | 0.46189 | 0.64514 | 0.72054 | 0.86492 | 0.64262 | 0.96025 | 0.73402 | 0.83421
Chart: RGB + Hillshade
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28
Train | 0.76987 | 0.68337 | 0.64932 | 0.6354 | 0.6085 | 0.58357 | 0.57024 | 0.56242 | 0.55696 | 0.54551 | 0.53649 | 0.53129 | 0.52353 | 0.47956 | 0.28821 | 0.2176 | 0.19267 | 0.18302 | 0.1759 | 0.16964 | 0.17426 | 0.16545 | 0.14278 | 0.13863 | 0.12915 | 0.12404 | 0.12945 | 0.12694
Val | 0.76091 | 0.68327 | 0.68498 | 0.66202 | 0.65564 | 0.67746 | 0.65411 | 0.64235 | 0.62274 | 0.72335 | 0.64855 | 0.65338 | 0.64056 | 0.59921 | 1.2916 | 0.49806 | 1.0409 | 1.3965 | 0.57221 | 0.56698 | 1.0291 | 1.0413 | 0.90834 | 1.1569 | 1.1537 | 0.94765 | 1.0735 | 0.79632
Chart: RGB + Slope
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21
Train | 0.74559 | 0.65999 | 0.62746 | 0.61537 | 0.60322 | 0.57625 | 0.56583 | 0.55444 | 0.54636 | 0.54011 | 0.52857 | 0.5174 | 0.42749 | 0.34143 | 0.29669 | 0.21166 | 0.18473 | 0.17668 | 0.17261 | 0.15361 | 0.17036
Val | 0.69557 | 0.65781 | 0.66119 | 0.64109 | 0.64172 | 0.68159 | 0.62761 | 0.65038 | 0.61174 | 0.62332 | 0.66894 | 0.57437 | 0.4328 | 0.60738 | 0.49422 | 0.42994 | 0.48473 | 0.52622 | 0.46283 | 0.45425 | 0.48704
Results
Configuration | Acc. | Prec. | Recall | F1
RGB | 0.972 | 0.440 | 0.949 | 0.599
RGB + DTM ★ | 0.985 | 0.593 | 0.825 | 0.690
Site 11 (Uthuwan Kanda) | 0.987 | 0.663 | 0.911 | 0.768
Site 12 (Victoria Reservoir) | 0.982 | 0.522 | 0.738 | 0.612
RGB + Hillshade | 0.970 | 0.420 | 0.932 | 0.577
RGB + Slope | 0.972 | 0.439 | 0.911 | 0.589
Table 1: Overall metrics on held-out sites 11 and 12. ★ = best-performing configuration (highest F1).
Performance Comparison
Chart: 
| RGB | RGB + DTM | RGB + Hillshade | RGB + Slope
Precision | 0.44 | 0.593 | 0.42 | 0.439
Recall | 0.949 | 0.825 | 0.932 | 0.911
F1 Score | 0.599 | 0.69 | 0.577 | 0.589
Figure 2: RGB + DTM achieves the best F1 (0.690); hillshade underperforms the RGB-only baseline despite deriving from the same DTM.
Discussion
All four configurations now produce functional detectors — recall ranges 0.825–0.949 and F1 ranges 0.577–0.690 across every variant, with none collapsing to background-only as in an earlier run with an inverted pos_weight. Recall is deliberately weighted above precision, favoring catching real landslides over avoiding false alarms. Raw elevation gives the clearest gain: RGB + DTM has the best F1 (0.690) and precision (0.593), improving on the RGB-only baseline (F1 0.599) mainly by reducing false positives — though performance still varies by site (F1 0.768 on Site 11 vs 0.612 on Site 12). Hillshade and slope underperform DTM: despite deriving from the same elevation model, hillshade actually falls below the RGB-only baseline (F1 0.577), suggesting raw elevation carries more usable signal for the network than either derived product. Accuracy is uninformative here: all four models score 97.0–98.5% accuracy since landslide pixels are a small minority class; F1 and Recall remain the decisive metrics.
Outlook and Next Steps
1. Sweep the sigmoid threshold to trade recall for precision, especially for RGB + DTM 2. Test feature fusion (e.g. RGB + DTM + Slope) now that single features are validated independently 3. Investigate why hillshade underperforms slope and DTM despite deriving from the same elevation model 4. Site-stratified cross-validation to reduce site-to-site F1 variance (0.768 vs 0.612 on RGB + DTM) 5. Revisit foundation-model backbones (DOFA, SkySense) now that a reliable ResNet50 U-Net baseline exists 6. Extend full-site inference to additional held-out sites as more annotated data becomes available
References
[1] Ronneberger et al. (2015). U-Net: CNNs for Biomedical Image Segmentation. MICCAI.
[2] Ghorbanzadeh et al. (2021). Evaluation of ML Methods for Landslide Detection. Remote Sensing, 11(2).
[3] Prakash et al. (2020). CNN-Based Approach for Spectral-Spatial Image Classification. Remote Sensing, 12(6).
[4] Chen et al. (2018). DeepLab: Semantic Segmentation with Deep Convolutional Nets. IEEE TPAMI, 40(4).
Project Repository
Data and code publicly available
github.com/nimesh7814/landslide_extraction